## Slide 1: Adaptive meshing using higher order hierarchic finite elements in static magnetic analysis
Akihisa Kameari
2025/09/10

## Slide 2: Higher order hierarchic finite elements
High order Nedelec elements with local complete sequence properties
J. Schoberl and S. Zaglmayr, COMPEL Vol. 24, No. 2 (2006)
各節点、辺、面、体要素の各オーダーで完全性が成り立つ
各辺、面、体で独立なオーダーの要素が使える。
通常、
De Rham complex
global complete sequence property
local complete sequence property

## Slide 3: Higher order hierarchic finite elements
4面体高次Hcurl要素の自由度

## Slide 4: Adaptive meshing using higher order hierarchic finite elements
Initial Mesh
Ne=150, Ndof=783,Nnonzero=26111
Mesh after 10 Refinement
Ne=243903, Ndof=1108002,
Nnonzero=53237796
(Ω-Ωｒ法）
feOrder=3

## Slide 5: 2 Potential Methods in static magnetic analysis
Python program using Netgen/Ngsolve

## Slide 6: Error estimation in Ω region
Magnetic scalar potential
Error estimation （Ω region）
In Ngsolve
fes = HDiv(mesh, order=feOrder-1, definedon=****)
Bd=GridFunction(fes)
Bd.Set(B)

## Slide 7: Error estimation in A region
Magnetic vector potential
Error estimation
In Ngsolve
fes = HCurl(mesh, order=feOrder-1, definedon=****)
Hd=GridFunction(fes)
Hd.Set(H)

## Slide 8: Adaptive meshing
Refinement
https://docu.ngsolve.org/latest/i-tutorials/unit-1.6-adaptivity/adaptivity.html
Zienkiewicz-Zhu type error estimator
Reference

## Slide 9: 磁性直方体中心磁場 Bz0
一点の磁場は滑らかに収束しない。特に、二次要素では精度が出ない。４次要素は計算時間がかかる
A-Ar法とA-Ωr法ではほぼ一致
A-Ωr法で磁性体表面をA-Ωr境界に一致させると精度が出ない。
中心点は節点上にあり取り扱いが問題か
*磁性体表面をA-Ωr境界とする
評価点(0,0,0)近傍は細分割されない。
磁場は一様で誤差が小さいと評価される。

## Slide 10: 磁性直方体内の磁気エネルギー積分 Wm
細分に関して滑らかに収束
Ω-Ωr法、 A-Ωr法＊は上から、A-Ar法, A-Ωr法は下から収束
値はCubeの１/４

## Slide 11: 計算時間と磁気エネルギー Wm
Ω-Ωr法、Order 3が同じ計算時間で高精度
誤差はΩ-Ωr法、Order 3時、ほぼ計算時間に反比例
A-Ar,A-Ωr法はほぼ一致。細分はほとんどA領域で行われる。A-Ωr法ではICCG法が発散するため残差最小を求めるのに時間を要する。
A-Ωr法は精度が悪い。
Adaptive meshinngにより０．０１%の精度が得られる！
計算時間は行列コレスキー分解とICCG法繰り返し時間
Adaptive meshingにより

## Slide 12: Adaptive meshing with Kelvin transformation
Initial mesh
Mesh after 6 adaptive refinements by Ω-Ωr.
Kelvin outer region
Inner region
Simultaneous adaptive refinement of Inner Kelvin outer regions.
Use Identify and Periodic in Ngsolve

## Slide 13: Adaptive meshing with Kelvin transformation
No dependence on the Kelvin radius rk.
Slower with Kelvin transformation.
Issues in refinements in Kelvin transformation region?

## Slide 14: Adaptive meshing with Kelvin transformation
Mesh after 7 adaptive refinements by A-Ar.
・角点近傍の細分
・Kervin領域原点（無限遠に相当）の細分
・Initial meshに依存する
Initial mesh